Mustek Digital Camera

##### Host Interface Specification

MDC-800  USB

###### Data: 1999/3/24

CATALOG

1. intorduction	2

2. Camera Behavior In Terms Of Host Interface	3

2.1 Camera States	3

2.2 Hardware Protocol Information	3

2.3 Command Format	3

3. DATA FORMATS	5

3.1 Quality, Resolution, Filesize, Frame	5

3.2 File Structure On CF-Card/Internal Memory	5

3.3 Huffman_Table, JPG_Header, Start_of_Frame, Start_of_Scan	6

3.4 Data Stored On Compact Flash Card (CF-Card)	9

3.5 Data Stored On Internal Memory	11

4. FILE ORGANIZATION	16

4.1 File Name	16

4.2 File Access	16

5. COMMANDS	18

5.1 Command Description	19

1. INTRODUCTION

This document describes the detailed host interface commands of the Mustek Digital Camera.

1.1 Purpose

This document specifies the communications interface between the host computer and the Digital Camera. This includes all camera commands, data, and control flow between the host and cameras.

1.2 Scope

This document completely specifies the behavior of the product feature set and the concepts. Future changes to the design and/or future additional functionality to these products will be documented in future specifications.

1.3 Intended Audience

This document is intended for any individuals who are involved in the development of software and firmware of the Digital Camera product. This document is also intended to assist future software/firmware developers involved in the support of these products.

2. Camera Behavior In Terms Of Host Interface

2.1 Camera States

The camera is always in exactly one of the following modes.

- Camera mode

- Playback mode

- VCam mode

If the camera isn’t connected to PC through RS-232 or USB, the user can toggle switch the mode by push the CAMERA/PLAYBACK button on the camera. Only if the camera is connected to PC through USB, the camera changed to VCam mode by S/W driver.

When the user connect DSC to PC through RS-232 or USB and launch Mustek S/W to communicate with the camera, all button operations except the power switch are ignored. To capture an image, the operator has to use the host software. If the camera detects both active USB and RS232 cable inserted, the camera deactivate RS232 and starts communicating though USB.

2.2 Hardware Protocol Information

Mustek DSC supports USB, with a maximum communication speed of 12M bits per second. The USB controller Net2888 supports four EndPoints. The behavior of EndPoint1 (Interrupt) is the same as other bulk endpoints.

| EndPoint | Transfer type | Max. Packet Size | Direction | Function |
| --- | --- | --- | --- | --- |
| 0 | Bulk | 8 Bytes | OUT | Command |
| 1 | Interrupt | 8 Bytes | IN | Status |
| 2 | Bulk | 64 Bytes | OUT | Upload to DSC |
| 3 | Bulk | 64 Bytes | IN | Download to PC |

2.3 Command Format

It’s always the host which issues commands. Host interface commands consist of 8 bytes of data. There are two kinds of command format:

(1) The first six bytes format is the same as RS-232. The last two byte are always zero (for most commands (see section 5.1)).

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | Command |
| 2 | Parameter1 or 0 |
| 3 | Parameter2 or 0 |
| 4 | Parameter3 or 0 |
| 5 | 0xAA |
| 6 | 0x00 |
| 7 | 0x00 |

(2) The first byte is 0x55, and second byte is Command ID. From third byte to 8’s byte is parameter or 0 (only 0x3F, 0x45 command used).

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | Command |
| 2 | Parameter1 or 0 |
| 3 | Parameter2 or 0 |
| 4 | Parameter3 or 0 |
| 5 | Parameter4 or 0 |
| 6 | Parameter5 or 0 |
| 7 | Parameter6 or 0 |

The camera responds ACK to the EndPoint0 (EP0) command packet sent from the host if the command is received correctly. And NAK if DSC can’t receive the command successfully. At most time host get READY status from EndPoint1 (EP1) if the camera is ready for commands or BUSY status if the camera is busy. Except exist when some query commands are sent, query result is returned through EP1 in these cases. If the host miss the result data, the host must re-send command after predefined maximum retry. And return FAIL to higher S/W layer driver after predefined maximum re-send command.

3. DATA FORMATS

The Mustek DSC supports both internal image storage and Compact Flash Card (CF-Card) storage.

3.1 Quality, Resolution, File Size, Frame

3.1.1 Image File

- Quality: Economic, Standard, and High quality.

- Resolution: 506x384 (Economic quality), 1012x768 (Standard and High quality).

- File Size: 48KB (Economic quality), 128KB (Standard quality), and 320KB (High quality).

3.1.2 Thumbnail of Image

- Resolution: 112x96.

- File Size: 4KB.

3.1.3 Video File

- Resolution: 112x96.

- File Size: 320KB.

- Frame: 64 frames.

3.1.4 Thumbnail of Video

- Resolution: 112x96.

- File Size: 8KB.

3.2 File Structure On CF-Card/Internal Memory

3.2.1 Thumbnail and Image File

|  | ↑ |  | ←JPG_Header |
| --- | --- | --- | --- |
| 4096 bytes |  | ←Table of Thumbnail |
|  |  | ←Thumbnail Data |
|  | ↓ |  |  |
| 1024 bytes | → |  | ←Table of Image |
|  |  | ←Compress Image Data |

- The total size of ‘JPG_Header’, ‘Table of Thumbnail’, and ‘Thumbnail Data’ are 4096 bytes. It means if get thumbnail, the size is 4096 bytes.

- The size of ‘Table of Image’ is 1024 bytes.

- If the file stored on CF-Card, then it’s must be standard JPEG file.

- In JPEG format, the compress data is end by 2 bytes (0xFF, 0xD9), but in DSC sometimes it must be add some 0xFF behind 0xFF and 0xD9, because the file size must be divide by 512, in order to transfer between host and DSC. So, for compress data of thumbnail and image finished (0xFF, 0xD9) it must be add some 0xFF bytes.

3.2.2 Video File

|  | ←1st Frame JPG_Header |
| --- | --- |
|  | ←1st Frame Table |
|  | ←1st Frame Compress Data |
|  | ←2nd Frame (Only Compress Data) |
|  | ←3rd Frame (Only Compress Data) |
| ‧ | ‧ |
| ‧ | ‧ |
| ‧ | ‧ |
|  | ←64th Frame (Only Compress Data) |

- The 1st frame is a standard JPEG format, if data stored on CF-Card.

- From 2nd frame to 64th frame only have compress data.

- Each frame size is different. But total size is 320KB.

- It used 1st frame image to do thumbnail. But the thumbnail of video size (8KB) is larger then 1st frame size. The reason is make sue that the 1st frame can be included.

- In JPEG format, the compress data is end by 2 bytes (0xFF, 0xD9), but in DSC sometimes it must be add some 0xFF behind 0xFF and 0xD9, because the file size must be divide by 512, in order to transfer between host and DSC. So, for each frame’s compress data finished (0xFF, 0xD9) it must be add some 0xFF bytes.

3.3 Huffman_Table, JPG_Header, Start_of_Frame, Start_of_Scan

There are some table used. As following :

BYTE Huffman_Tab[424] = 		{ 0xFF,0xC4,0x01,0xA2,

/* DC_Luminance_Bits */

0, 0, 1, 5, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0, 0, 0,

/* DC_Luminance_Value */

0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 0x0A, 0x0B,

/* DC_Chrominance_Bits */

1, 0, 3, 1, 1, 1, 1, 1, 1, 1, 1, 1, 0, 0, 0, 0, 0,

/* DC_Chrominance_Value */

0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 0x0A, 0x0B,

/* AC_Luminance_Bits */

0x10, 0, 2, 1, 3, 3, 2, 4, 3, 5, 5, 4, 4, 0, 0, 1, 0x7D,

/* AC_Luminance_Value */

0x01, 0x02, 0x03, 0x00, 0x04, 0x11, 0x05, 0x12,

0x21, 0x31, 0x41, 0x06, 0x13, 0x51, 0x61, 0x07,

0x22, 0x71, 0x14, 0x32, 0x81, 0x91, 0xA1, 0x08,

0x23, 0x42, 0xB1, 0xC1, 0x15, 0x52, 0xD1, 0xF0,

0x24, 0x33, 0x62, 0x72, 0x82, 0x09, 0x0A, 0x16,

0x17, 0x18, 0x19, 0x1A, 0x25, 0x26, 0x27, 0x28,

0x29, 0x2A, 0x34, 0x35, 0x36, 0x37, 0x38, 0x39,

0x3A, 0x43, 0x44, 0x45, 0x46, 0x47, 0x48, 0x49,

0x4A, 0x53, 0x54, 0x55, 0x56, 0x57, 0x58, 0x59,

0x5A, 0x63, 0x64, 0x65, 0x66, 0x67, 0x68, 0x69,

0x6A, 0x73, 0x74, 0x75, 0x76, 0x77, 0x78, 0x79,

0x7A, 0x83, 0x84, 0x85, 0x86, 0x87, 0x88, 0x89,

0x8A, 0x92, 0x93, 0x94, 0x95, 0x96, 0x97, 0x98,

0x99, 0x9A, 0xA2, 0xA3, 0xA4, 0xA5, 0xA6, 0xA7,

0xA8, 0xA9, 0xAA, 0xB2, 0xB3, 0xB4, 0xB5, 0xB6,

0xB7, 0xB8, 0xB9, 0xBA, 0xC2, 0xC3, 0xC4, 0xC5,

0xC6, 0xC7, 0xC8, 0xC9, 0xCA, 0xD2, 0xD3, 0xD4,

0xD5, 0xD6, 0xD7, 0xD8, 0xD9, 0xDA, 0xE1, 0xE2,

0xE3, 0xE4, 0xE5, 0xE6, 0xE7, 0xE8, 0xE9, 0xEA,

0xF1, 0xF2, 0xF3, 0xF4, 0xF5, 0xF6, 0xF7, 0xF8, 0xF9, 0xFA,

/* AC_Chrominance_Bits */

0x11, 0, 2, 1, 2, 4, 4, 3, 4, 7, 5, 4, 4, 0, 1, 2, 0x77,

/* AC_Chrominance_Value */

0x00, 0x01, 0x02, 0x03, 0x11, 0x04, 0x05, 0x21,

0x31, 0x06, 0x12, 0x41, 0x51, 0x07, 0x61, 0x71,

0x13, 0x22, 0x32, 0x81, 0x08, 0x14, 0x42, 0x91,

0xA1, 0xB1, 0xC1, 0x09, 0x23, 0x33, 0x52, 0xF0,

0x15, 0x62, 0x72, 0xD1, 0x0A, 0x16, 0x24, 0x34,

0xE1, 0x25, 0xF1, 0x17, 0x18, 0x19, 0x1A, 0x26,

0x27, 0x28, 0x29, 0x2A, 0x35, 0x36, 0x37, 0x38,

0x39, 0x3A, 0x43, 0x44, 0x45, 0x46, 0x47, 0x48,

0x49, 0x4A, 0x53, 0x54, 0x55, 0x56, 0x57, 0x58,

0x59, 0x5A, 0x63, 0x64, 0x65, 0x66, 0x67, 0x68,

0x69, 0x6A, 0x73, 0x74, 0x75, 0x76, 0x77, 0x78,

0x79, 0x7A, 0x82, 0x83, 0x84, 0x85, 0x86, 0x87,

0x88, 0x89, 0x8A, 0x92, 0x93, 0x94, 0x95, 0x96,

0x97, 0x98, 0x99, 0x9A, 0xA2, 0xA3, 0xA4, 0xA5,

0xA6, 0xA7, 0xA8, 0xA9, 0xAA, 0xB2, 0xB3, 0xB4,

0xB5, 0xB6, 0xB7, 0xB8, 0xB9, 0xBA, 0xC2, 0xC3,

0xC4, 0xC5, 0xC6, 0xC7, 0xC8, 0xC9, 0xCA, 0xD2,

0xD3, 0xD4, 0xD5, 0xD6, 0xD7, 0xD8, 0xD9, 0xDA,

0xE2, 0xE3, 0xE4, 0xE5, 0xE6, 0xE7, 0xE8, 0xE9,

0xEA, 0xF2, 0xF3, 0xF4, 0xF5, 0xF6, 0xF7, 0xF8, 0xF9, 0xFA,

/* Blank data */

0xFF, 0xFE, 0x01, 0x8F};

BYTE File_Header[41]={/* JPG file start marker */

0xFF, 0xD8,

/* Application marker */

0xFF, 0xE0, 0x00, 0x10, 0x4A, 0x46, 0x49, 0x46, 0x00, 0x01,

0x00, 0x01, 0x00, 0x48, 0x00, 0x48, 0x00, 0x00,

/* Application marker */

0xFF, 0xE1, 0x00, 0x0E, 0x43, 0x41, 0x4D, 0x2D, 0x4D, 0x44,

0x43, 0x38, 0x30, 0x30, 0x00, 0x00,

/* Quantization table marker */

0xFF, 0xDB, 0x00, 0x84, 0x00};

BYTE File_Header1[24]={/* JPG file start marker */

0xFF, 0xD8,

/* Application marker */

0xFF, 0xE0, 0x00, 0x10, 0x4A, 0x46, 0x49, 0x46, 0x00,	 0x01,

0x00, 0x01, 0x00, 0x48, 		0x00, 0x48, 0x00, 0x00,

/* Application marker */

0xFF, 0xE1, 	0x0F, 0xEC};

BYTE File_Header2[34]={/* JPG file start marker */

0xFF, 0xD8,

/* Application marker */

0xFF, 0xE0, 0x00, 0x10, 0x4A, 0x46, 0x49, 0x46, 0x00, 0x01,

0x00, 0x01, 0x00, 0x48,	 	0x00, 0x48, 0x00, 0x00,

/* Application marker */

0xFF, 0xE1, 0x00, 0x0E, 0x43, 0x41, 0x4D, 0x2D, 0x4D, 0x44,

0x43, 0x38, 0x30, 0x30};

//For Thumbnail: 112x96

BYTE SOF_SOS1[33]={ /* Start of frame marker */

0xFF, 0xC0, 0x00, 0x11, 0x08, 0x00, 0x60, 0x00, 0x70, 0x03,

0x01, 0x21, 0x00, 0x02, 0x11, 0x01, 0x03, 0x11, 0x01,

/* Start of scan marker */

0xFF, 0xDA, 0x00, 0x0C, 0x03, 0x01, 0x00, 0x02, 0x11, 0x03,

0x11, 0x00, 0x3F, 0x00};

//For Economic quality image: 506x384

BYTE SOF_SOS2[33]={ /* Start of frame marker */

0xFF, 0xC0, 0x00, 0x11, 0x08, 0x01, 0x80, 0x01, 0xFA, 0x03,

0x01, 0x21, 0x00, 0x02, 0x11, 0x01, 0x03, 0x11, 0x01,

/* Start of scan marker */

0xFF, 0xDA, 0x00, 0x0C, 0x03, 0x01, 0x00, 0x02, 0x11, 0x03,

0x11, 0x00, 0x3F, 0x00};

//For Standard and High quality image: 1012x768

BYTE SOF_SOS3[33]={ /* Start of frame marker */

0xFF, 0xC0, 0x00, 0x11, 0x08, 0x03, 0x00, 0x03, 0xF4, 0x03,

0x01, 0x21, 0x00, 0x02, 0x11, 0x01, 0x03, 0x11, 0x01,

/* Start of scan marker */

0xFF, 0xDA, 0x00, 0x0C, 0x03, 0x01, 0x00, 0x02, 0x11, 0x03,

0x11, 0x00, 0x3F, 0x00};

3.4 Data Stored On Compact Flash Card (CF-Card)

All images are stored as DOS files on Compact Flash Card. The image data is stored in JPEG and stored under “\DSCIMG” directory.

- All image files stored on CF-Card are standard JPEG files.

- The 36th byte is record the image quality.

- Each image data is stored with unique file name assigned automatically.

3.4.1 Image File

|  | ↑ |  | ←JPG_Header |
| --- | --- | --- | --- |
| 4096bytes |  | ←Table of Thumbnail |
|  |  | ←Thumbnail Data |
|  | ↓ |  |  |
| 1024bytes | → |  | ←Table of Image |
|  |  | ←Compress Image Data |

- All data stored on CF-Card are correct.

- If get an image from CF-Card:

- All data will be transfer.

3.4.2 Thumbnail of Image

|  | ↑ |  | ←JPG_Header |
| --- | --- | --- | --- |
| 4096bytes |  | ←Table of Thumbnail |
|  |  | ←Thumbnail Data |
|  | ↓ |  |  |
| 1024bytes | → |  | ←Table of Image |
|  |  | ←Compress Image Data |

- All data stored on CF-Card are correct.

- If get a thumbnail of image from CF-Card:

- Only ‘JPG_Header’, ‘Table of Thumbnail’, and ‘Thumbnail Data’ will be transfer. So the thumbnail size is 4096 bytes.

- In JPG_Header, the ‘Application marker (0xFF, 0xE1)’ length value included the length of ‘Table of Thumbnail’ and ‘Thumbnail Data’.

- In order to read correct data, it must be change the ‘Application marker (0xFF, 0xE1)’ length value: the 23rd and 24th byte data.

Assume: lpData is a pointer, and point to the start of data

Function:

*(lpData+ 22) =0x00;  // change the ‘Application marker’ length

*(lpData+ 23) =0x0E;

3.4.3 Video File

|  | ←1st Frame JPG_Header |
| --- | --- |
|  | ←1st Frame Table |
|  | ←1st Frame Compress Data |
|  | ←2nd Frame (Only Compress Data) |
|  | ←3rd Frame (Only Compress Data) |
| ‧ | ‧ |
| ‧ | ‧ |
| ‧ | ‧ |
|  | ←64th Frame (Only Compress Data) |

- All data stored on CF-Card are correct.

- If get a video file from CF-Card:

‧All data will be transfer.

3.4.4 Thumbnail of Video

|  | ←1st Frame JPG_Header |
| --- | --- |
|  | ←1st Frame Table |
|  | ←1st Frame Compress Data |
|  | ←2nd Frame (Only Compress Data) |
|  | ←3rd frame (Only Compress Data) |
| ‧ | ‧ |
| ‧ | ‧ |
| ‧ | ‧ |
|  | ←64th Frame (Only Compress Data) |

- All data stored on CF-Card are correct.

- If get a thumbnail of video from CF-Card:

- It used 1st frame image to do thumbnail.

- Only 1st frame ‘JPG_Header’, ‘Table’, and ‘Compress Data’ will be used.

- Because each frame size is different. The thumbnail of video size is define 8KB, in order to make sure that 1st frame can be included. Sometimes the DSC will transfer a part of 2nd frame compress data. But it had no effect.

- In ‘JPG_Header’, the ‘Application marker’ length value must be change:

Assume : The thumbnail of video transfer finished and stored in memory(PC),

lpData is a pointer, and point to the start of thumbnail of video data

Function :

*(lpData+ 22) =0x00;  // change the ‘Application marker’ length

*(lpData+ 23) =0x0E;

3.5 Data Stored On Internal Memory

|  | Image |  | Video |  |
| --- | --- | --- | --- | --- |
|  | ↑ | Not correct | ←JPG_Header | Not correct | ←1st Frame JPG_Header |
| 4096bytes | Not correct | ←Table of Thumbnail | Not correct | ←1st Frame Table |
|  |  | ←Thumbnail Data |  | ←1st Frame Compress Data |
|  | ↓ |  |  |  |  |
| 1024bytes | → | Not correct | ←Table of Image |  | ←2nd Frame(Compress Data) |
|  |  | ←Compress Image Data |  | ←3rd Frame(Compress Data) |
|  |  |  | ‧ | ‧ |
|  |  |  | ‧ | ‧ |
|  |  |  | ‧ | ‧ |
|  |  |  |  | ←64th Frame(Compress Data) |

Data stored on internal memory have some different with CF-Card.

- For image file:

- The data of ‘Thumbnail Data’ and ‘Compress Image Data’ are correct.

- The total size of ‘JPG_Header’, ‘Table of Thumbnail’, and ‘Thumbnail Data’ are 4096 bytes.

- The size of ‘Table of Image’ is 1024 bytes.

- The 36th byte is correct in ‘JPG_Header’, it’s record the image quality.

- The Quantization_Table (128 bytes) is almost correct, but the second Quantization_Table index is wrong.

- Other tables have wrong data, like JPG_Header, Huffman_Table, Start_of_Frame, Start_of_Scan.

- After transfer data from Internal Memory it must be fill the correct JPG_Header, , Huffman_Table, Start_of_Frame, Start_of_Scan tables (see section 3.3) and the second Quantization_Table index.

- For video file:

- The data of each frame’s ‘Compress Data’ is correct.

- Each frame size is different, but total size is 320KB.

- The Quantization_Table (128 bytes) is almost correct, but the second Quantization_Table index is wrong.

- Other tables have wrong data, like JPG_Header, Huffman_Table, Start_of_Frame, Start_of_Scan.

- After transfer data from Internal Memory it must be fill the correct JPG_Header, , Huffman_Table, Start_of_Frame, Start_of_Scan tables (see section 3.3) and the second Quantization_Table index.

3.5.1 How to know the correct image quality

- The 36th byte is recorded the image quality.

Assume : The image data transfer finished and stored in memory(PC),

lpData is a pointer, and point to the start of image data

Function :

Quality = *(lpData+35);

If Quality = 0 → The quality is Economic.

If Quality = 1 → The quality is Standard.

If Quality = 2 → The quality is High.

3.5.2 Image File

|  | ↑ | Not correct | ←JPG_Header |
| --- | --- | --- | --- |
| 4096bytes | Not correct | ←Table of Thumbnail |
|  |  | ←Thumbnail Data |
|  | ↓ |  |  |
| 1024bytes | → | Not correct | ←Table of Image |
|  |  | ←Compress Image Data |

- If get an image from Internal Memory:

- All data will be transfer.

- The data of ‘JPG_Header’ and ‘Table of Image’ are wrong, it must be fill correct data. The ‘Table of Thumbnail’ is not necessary to fill, because it’s not used if get an image.

Assume : The image data transfer finished and stored in memory(PC),

lpData is a pointer, and point to the start of data

Function :

memcpy(lpData,File_Header1,24);  // fill JPG_Header

lpData += 4096;  // escape the thumbnail

memcpy(lpData,File_Header,41);  // fill JPG_Header

*lpData = *(lpData+1) = 0;  // the second Quantization_Table index

*(lpData+105) = 1;  // the second Q_Table index

lpData += 170;

memcpy(lpData,Huffman_Tab,424);  // fill Huffman_Table

lpData += 821;

if (image is Economic : 506x384)

memcpy(lpData,SOF_SOS2,33);  // fill Start_of_Frame, Start_of_Scan

if (image is Standard or High : 1012x768)

memcpy(lpData,SOF_SOS3,33);  // fill Start_of_Frame, Start_of_Scan

3.5.3 The Thumbnail of Image

|  | ↑ | Not correct | ←JPG_Header |
| --- | --- | --- | --- |
| 4096bytes | Not correct | ←Table of Thumbnail |
|  |  | ←Thumbnail Data |
|  | ↓ |  |  |
| 1024bytes | → | Not correct | ←Table of Image |
|  |  | ←Compress Image Data |

- If get thumbnail of image from Internal Memory:

- Only ‘JPG_Header’, ‘Table of Thumbnail’, and ‘Thumbnail Data’ will be transfer. So the thumbnail size is 4096 bytes.

- The data of ‘JPG_Header’ and ‘Table of Thumbnail’ are wrong, it must be fill correct data:

Assume : The thumbnail of image data transfer finished and stored in memory(PC),

lpData is a pointer, and point to the start of data

Function :

memcpy(lpData,File_Header,41);  // fill JPG_Header

*(lpData+105) = 1;		  // the second Quantization_Table index

lpData += 170;

memcpy(lpData,Huffman_Tab,424);  // fill Huffman_Table

lpData += 821;

memcpy(lpData,SOF_SOS1,33);  // fill Start_of_Frame, Start_of_Scan

3.5.4 Video File

| Not correct | ←1st Frame JPG_Header |
| --- | --- |
| Not correct | ←1st Frame Table |
|  | ←1st Frame Compress Data |
|  | ←2nd Frame (Only Compress Data) |
|  | ←3rd Frame (Only Compress Data) |
| ‧ | ‧ |
| ‧ | ‧ |
| ‧ | ‧ |
|  | ←64th Frame (Only Compress Data) |

- If get video file from Internal Memory:

- All data will be transfer.

- In 1st frame, the data of ‘JPG_Header’ and ‘Table’ are wrong. It must be fill correct data.

Assume : The video data transfer finished and stored in memory(PC),

lpData is a pointer, and point to the start of data

Function :

memcpy(lpData,File_Header2,34);  // fill JPG_Header

*(lpData+36) = (char)0xFF;  // fill Quantization_Table marker

*(lpData+37) = (char)0xDB;

*(lpData+38) = 0;

*(lpData+39) = (char)0x84;

*(lpData+40) = 0;

*(lpData+105) = 1;  // the second Quzntization_Table index

lpData += 170;

memcpy(lpData,Huffman_Tab,424);  // fill Huffman_Table

lpData += 821;

memcpy(lpData,SOF_SOS1,33);  // fill Start_of_Frame, Start_of_Scan

3.5.5 Thumbnail of Video

| Not correct | ←1st Frame JPG_Header |
| --- | --- |
| Not correct | ←1st Frame Table |
|  | ←1st Frame Compress Data |
|  | ←2nd Frame (Only Compress Data) |
|  | ←3rd Frame (Only Compress Data) |
| ‧ | ‧ |
| ‧ | ‧ |
| ‧ | ‧ |
|  | ←64th Frame (Only Compress Data) |

- If get thumbnail of video from Internal Memory:

- It used 1st frame image to do thumbnail.

- Only 1st frame ‘JPG_Header’, ‘Table’, and ‘Compress Data’ will be used.

- Each frame size is different. The thumbnail of video size is define 8KB, in order to make sure that 1st frame can be included. Sometimes the DSC will transfer a part of 2nd frame compress data. But it had no effect.

- In 1st frame, the data of ‘JPG_Header’ and ‘Table’ are wrong. It must be fill correct data.

Assume : The thumbnail of video data transfer finished and stored in memory(PC),

lpData is a pointer, and point to the start of data

Function :

memcpy(lpData,File_Header,41);  // fill JPG_Header

*(lpData+105) = 1;		  // the second Q_Table index

lpData += 170;

memcpy(lpData,Huffman_Tab,424);  // fill Huffman_Table

lpData += 821;

memcpy(lpData,SOF_SOS1,33);  // fill Start_of_Frame, Start_of_Scan

4. FILE ORGANIZATION

This chapter describes file organization for the internal control and the CF-Card and naming rules for the image files. All images on the CF-Card are stored as DOS files. The maximum number of image files on CF-Card is limited to 999 regardless of memory size of the card.

4.1 File Name

4.1.1 File Name on Card and File Name Number

‧All the image files on Compact Flash card are stored as DOS files with following naming convention: \DSCIMG\IMG_nnnn.JPG

- All the video files on Compact Flash card are stored as DOS files with following naming convention: \DSCIMG\VDO_nnnn.JPG

‧nnnn : Serial number that starts with 0001, and is assigned by the camera firmware in a ever-increasing fashion until wraparound occurs.

Note that different memory cards can be used with a single camera. When the CF-Card inserted and there are some images on it, the FW will re-sort the image file in “DSCIMG” directory and given a serial number of image filename. If the “DSCIMG” directory does not exist in insert CF-Card, the FW will make a “DSCIMG” directory and store image file in it. The serial number for the image just taken, the file name will be the biggest number in the card + 1.

The maximum file number is 999. If IMG_0999.JPG file already exists or not enough memory space on CF-Card, the DSC can not be shot. If an image is erased through the user interface on the camera or through host communication, the file names of other files will re-sort again, and let the number of filename is serial.

4.1.2 Picture Numbers Internal to the Camera

The picture number is sequentially assigned to images according to the exposed order in camera. If an image is erased via the camera user interface or host communication, the picture number is reassigned to the images which had bigger number than the erased image automatically in the camera. For example, camera has 4 images (#0, #1, #2 and #3). If #2 image is erased, the new picture number for the #3 image is assigned as #2, consequently the image numbers will be #0, #1 and #2.

None of this affects the serial number in the filenames at all, i.e., files are not renamed as a result of this internal gap removal.

4.2 File Access

4.2.1 Picture Number Access

The host is able to retrieve the file data, thumbnail data, and picture information by specifying the picture number.

4.2.2 File Data Transfer

- How to transfer file data bytes:

The DSC transfer data from internal memory(or CF-card) to the host by EndPoint3 with 64 bytes for each packets.

- Dummy data:

The first 64 bytes (first packet) are dummy data. So, if the image file have 48KB size, the DSC will transfer 64 bytes + 48KB.

‧When DSC receive the command correctly, it will be start to send data to host until transfer finish.

5. COMMANDS

The following list the commands that supported by USB interface of camera.

The command description is written from the view of host PC, so the term ‘Get’, ‘Download’ is transfer data from DSC to PC, and ‘Set’, ‘Upload’ is transfer data from PC to DSC.

| Code | Description | Mode |
| --- | --- | --- |
| 0x00 | Initialize connection |  |
| 0x01 | Get system status |  |
| 0x02 | Take a picture |  |
| 0x03 | Set target to image/thumbnail/video |  |
| 0x04 | Delete an image |  |
| 0x05 | Get a stored image |  |
| 0x07 | Get the file size of an image |  |
| 0x09 | Get the thumbnail of a stored image |  |
| 0x0C | Set frame index of playback 4 view down |  |
| 0x0D | Get number of total images in DSC |  |
| 0x0F | Set timer ON |  |
| 0x10 | Get the thumbnail of a storage video |  |
| 0x11 | Set Power Auto-OFF Disable (NO) |  |
| 0x12 | Set Playback mode |  |
| 0x14 | Set Power Auto-OFF Enable (YES) |  |
| 0x15 | Set timer OFF |  |
| 0x16 | Set Camera mode |  |
| 0x17 | Set DSC playback the specified image |  |
| 0x18 | Set Flash mode AUTO |  |
| 0x19 | Set Flash mode ON |  |
| 0x1A | Set Flash mode OFF |  |
| 0x1B | Set frame index of playback 4 view up |  |
| 0x1C | Set image Protect OFF |  |
| 0x1D | Set image Protect ON |  |
| 0x1E | Set Info display ON |  |
| 0x1F | Set Info display OFF |  |
| 0x20 | Get OSD W.B. / Exposure settings |  |
| 0x21 | Set Exposure value |  |
| 0x22 | Set WB light source |  |
| 0x23 | Set DSC TV system |  |
| 0x25 | Get remain free image count |  |
| 0x26 | Set 4 picture mode when playback |  |
| 0x27 | Set 1 picture mode when playback |  |
| 0x29 | Get protection status of specified image |  |
| 0x2A | Set LCD ON |  |
| 0x2B | Set LCD OFF |  |
| 0x2C | Set DSC Power OFF |  |
| 0x2D | Set Resolution/Quality |  |
| 0x2F | Set Menu disp ON |  |
| 0x30 | Set Menu disp OFF |  |
| 0x32 | Set storage source(CF-Card/internal) |  |
| 0x34 | Ack DSC disconnection(Enable buttons) |  |
| ※0x3E | Take shot in Fine mode (320x240) | VCam |
| 0x3F | Set DSC in Fine mode (320x240) and set take picture’s resolution | VCam |
| 0x40 | Take shot in Draft mode (320x80) | VCam |
| 0x41 | Set DSC in Draft mode (320x80) | VCam |
| 0x43 | Set Draft mode AGC_gain (320x80) | VCam |
| 0x44 | Set RGB_gain value | VCam |
| 0x45 | Set Exposure value and Draft mode Exposure value | VCam |
| 0x46 | Set AGC_gain | VCam |
| 0x47 | Get RGB_gain, AGC_gain, Exposure value setting from DSC | VCam |
| 0x49 | Get DSC Quality setting |  |
| 0x50 | Set exposure mode(MTRX/CNTR) |  |
| 0x51 | Get exposure mode(MTRX/CNTR) |  |
| 0x52 | Set image Saturation | VCam |

5.1 Command Description

This section describes commands supported by Mustek Multi-Function Digital Camera MDC-800.

5.1.1 Initialize connection (0x00)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x00 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command is to initialize communication with the DSC and disable all buttons on DSC exception the POWER button.

- Return：The DSC return 16 bytes information by EndPoint1. The first packet (8 bytes) is dummy data. And the second packet (8 bytes) is not dummy data, and the last 5 bytes are Firmware version in second packet (8 bytes).

5.1.2 Get system status (0x01)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x01 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command get DSC status.

- Return：The DSC return 16 bytes data by EndPoint1. The first packet (8 bytes) is dummy data. The second packet (8 bytes) is not dummy data, and only first 4 bytes are valid in second packet (8 bytes).

### First Byte

| Bit Offset | Description | Value Description |
| --- | --- | --- |
| 0 | CF-Card Status | 0 : card is inserted, 1 : card isn’t inserted |
| 1 | Reserved | Reserved |
| 2 | Battery status | 0 : Battery Normal, 1 : Battery Low |
| 3-7 | Reserved | Reserved |

### Second Byte

| Bit Offset | Description | Value Description |
| --- | --- | --- |
| 0 | OSD Menu flag | 0 : menu disable, 1 : menu enable |
| 1 | OSD Info flag | 0 : Info disable, 1 : Info enable |
| 2 | LCD status | 0 : LCD OFF, 1 : LCD ON |
| 3 | Auto-OFF flag | 0 : NO, 1 : YES |
| 4 | Vcam mode flag | 0 : Other(Check bit 5), 1 : Vcam mode |
| 5 | Camera mode flag | 0 : Playback mode, 1 : Camera mode |
| 6 | Timer flag | 0 : Timer disable, 1 : Timer enable |
| 7 | Playback view mode | 0 : 1 picture view, 1 : 4 Picture View |

### Third Byte

| Bit Offset | Description | Value Description |
| --- | --- | --- |
| 0-1 | Reserved | Reserved |
| 2 | TV System flag | 0 : PAL, 1 : NTSC |
| 3-7 | Reserved | Reserved |

### Fourth Byte

| Bit Offset | Description | Value Description |
| --- | --- | --- |
| 0 | Red-eye reduction | 0 : Disable, 1 : Enable |
| 1-2 | Flash setting | (bit 1,bit 2)：(0,0) is Flash Auto (1,0) is Flash ON (0,1) is Flash OFF |
| 3 | Reserved | Reserved |
| 4 | TV Output Connect flag | 0 : TV Output Disconnect, 1 : TV Output Connect |
| 5-7 | Reserved | Reserved |

5.1.3 Take shot (0x02)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x02 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to take a shot.

- Return：The DSC has no return value.

5.1.4 Set target (0x03)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x03 |
| 2 | Target ID (1:image,2:thumbnail,3:video,4:not setting) |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set target. For example, to get a thumbnail of video, the target must set to video.

- Return：The DSC has no return value.

5.1.5 Delete an image(0x04)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x04 |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to delete an image. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999.

- Return：The DSC has no return value.

5.1.6 Get a stored image (0x05)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x05 |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to get an image from DSC to the host. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999.

- Return：The DSC has no return value. When DSC receive the command correct, it will be start to transfer image data to host by EndPoint3.

5.1.7 Get the file size of an image (0x07)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x07 |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to get the file size of image. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999.

- Return：The DSC return 16 bytes data by EndPoint1. The first packet (8 bytes) is dummy data. The second packet (8 bytes) is not dummy data, and only first 3 bytes are valid in second packet (8 bytes). Filesize = data[0]*65536 + data[1]*256 + data[2] (bytes)

5.1.8 Get the thumbnail of a stored image (0x09)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x09 |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to get the thumbnail of image file. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999. To get video thumbnail, please use 0x10 code.

- Return：The DSC has no return value. When DSC receive this command correct, it will be start to transfer thumbnail data to host by EndPoint3.

5.1.9 Move down playback 4 pic index (0x0C)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x0C |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC change the selected index in playback 4-picture mode to simulate the Down button be pressed on DSC.

- Return：The DSC has no return value.

5.1.10 Get number of total images in DSC (0x0D)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x0D |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to send total images/videos files in DSC. If the target index is thumbnail, the return value is total images files. If the target index is video, the return value is total videos files.

- Return：The DSC return 16 bytes data by EndPoint1. The first packet (8 bytes) is dummy data. The second packet (8 bytes) is not dummy data, and only first 2 bytes are valid in second packet (8 bytes). Total files = data[0]*256 + data[1]

5.1.11 Set Timer ON (0x0F)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x0F |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set timer ON.

- Return：The DSC has no return value.

5.1.12 Get Video Thumbnail (0x10)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x10 |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to get the thumbnail of video file. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999. To get the thumbnail of image file, please use 0x09 code.

- Return：The DSC has no return value. When DSC receive this command correct, it will be start to transfer video thumbnail data to host by EndPoint3.

5.1.13 Set Auto-OFF : No (0x11)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x11 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to stay at POWER-ON state.

- Return：The DSC has no return value.

5.1.14 Set Playback mode (0x12)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x12 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC to Playback mode, and show the last picture on LCD.

- Return：The DSC has no return value.

5.1.15 Set Auto-OFF : Yes (0x14)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x14 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to power off automatically if no action is detected for more than 30 seconds.

- Return：The DSC has no return value.

5.1.16 Set Timer OFF (0x15)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x15 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set timer OFF.

- Return：The DSC has no return value.

5.1.17 Set Camera mode (0x16)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x16 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC to Camera mode.

- Return：The DSC has no return value.

5.1.18 Playback Num. # image (0x17)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x17 |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to display the image. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999.

- Return：The DSC has no return value.

5.1.19 Set Flash mode : AUTO (0x18)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x18 |
| 2 | Red-eye Flag |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC flash mode to AUTO. If the third byte is 1, Red-eye reduction will be enabled and if the byte is 0, Red-eye reduction will be disabled.

- Return：The DSC has no return value.

5.1.20 Set Flash mode : ON (0x19)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x19 |
| 2 | Red-eye Flag |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC flash mode to ON. If the third byte is 1, Red-eye reduction will be enabled and if the byte is 0, Red-eye reduction will be disabled.

- Return：The DSC has no return value.

5.1.21 Set Flash mode : OFF (0x1A)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x1A |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC flash mode to OFF.

- Return：The DSC has no return value.

5.1.22 Set frame index of playback 4 view up (0x1B)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x1B |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC change the selected index in playback 4-picture mode to simulate the Up button be pressed on DSC.

- Return：The DSC has no return value.

5.1.23 Set image Protect OFF (0x1C)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x1C |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set the image is unprotect. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999.

- Return：The DSC has no return value.

5.1.24 Set image Protect ON (0x1D)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x1D |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set the image is protect. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999.

- Return：The DSC has no return value.

5.1.25 Set Info display mode : ON (0x1E)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x1E |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC OSD information display mode to ON.

- Return：The DSC has no return value.

5.1.26 Set Info display mode : OFF (0x1F)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x1F |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC OSD information display mode to OFF.

- Return：The DSC has no return value.

5.1.27 Get OSD W.B. / Exposure settings (0x20)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x20 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command get the DSC OSD W.B. / Exposure settings.

- Return：The DSC return 16 bytes data by EndPoint1. The first packet (8 bytes) is dummy data. The second packet (8 bytes) is not dummy data, and the first 2 bytes are valid in second packet (8 bytes). The data[0] is W.B. setting, and data[1] is exposure setting.

5.1.28 Set Exposure value (0x21)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x21 |
| 2 | Exposure value |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set exposure value. The exposure value is from 0 to 4.

- Return：The DSC has no return value.

5.1.29 Set WB light source (0x22)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x22 |
| 2 | W.B. mode( 1：AUTO 2：INDOOR- 4：INDOOR+ 8：OUTDOOR) |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set W.B. mode.

- Return：The DSC has no return value.

5.1.30 Set DSC TV system (0x23)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x23 |
| 2 | TV source(0：PAL, 1：NTSC) |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set the DSC TV system.

- Return：The DSC has no return value.

5.1.31 Get remain free image count (0x25)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x25 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to get remain free image count.

- Return：The DSC return 16 bytes data by EndPoint1. The first packet (8 bytes) is dummy data. The second packet (8 bytes) is not dummy data, and only first 6 bytes are valid in second packet (8 bytes). The first and second byte is for H-quality image. The third and fourth byte is for S-quality image. The fifth and sixth byte is for E-quality image.

H-quality = (data[0]/16*1000)+((data[0]%16)*100)+(data[1]/16*10)+(data[1]%16)

S-quality = (data[2]/16*1000)+((data[2]%16)*100)+(data[3]/16*10)+(data[3]%16)

E-quality = (data[4]/16*1000)+((data[4]%16)*100)+(data[5]/16*10)+(data[5]%16)

5.1.32 Set 4 picture mode when playback (0x26)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x26 |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set 4 pictures mode when playback. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999.

- Return：The DSC has no return value.

5.1.33 Set 1 picture mode when playback (0x27)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x27 |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command set 1 picture mode when playback. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999.

- Return：The DSC has no return value.

5.1.34 Get protection status of specified image (0x29)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x29 |
| 2 | BCD Index (MSB) |
| 3 | BCD Index |
| 4 | BCD Index (LSB) |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

‧Function：The command get the specified image protection status. The index is presented in BCD form. For example, 123 is coded as 01 02 03. The maximum value is 999.

‧Return：The DSC return 16 bytes data by EndPoint1. The first packet (8 bytes) is dummy data. The second packet (8 bytes) is not dummy data, and only first byte is valid in second packet (8 bytes). If the data byte value is 1, then the image is protect. If the data byte value is 0, then the image is unprotect.

5.1.35 Set LCD ON (0x2A)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x2A |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set LCD ON.

- Return：The DSC has no return value.

5.1.36 Set LCD OFF (0x2B)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x2B |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set LCD OFF.

- Return：The DSC has no return value.

5.1.37 Set DSC Power OFF (0x2C)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x2C |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set POWER OFF.

- Return：The DSC has no return value.

5.1.38 Set Resolution/Quality (0x2D)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x2D |
| 2 | Image resolution/quality ID： 0：Economic, 1：Standard, 2：High |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set the image resolution/quality.

- Return：The DSC has no return value.

5.1.39 Set Menu display ON (0x2F)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x2F |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set menu display ON on LCD.

- Return：The DSC has no return value.

5.1.40 Set Menu display OFF (0x30)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x30 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set menu display OFF on LCD.

- Return：The DSC has no return value.

5.1.41 Set storage source(CF-Card/internal) (0x32)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x32 |
| 2 | Image source ID： 0：CF-Card, 1：Internal Memory |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set the storage source.

- Return：The DSC has no return value.

5.1.42 Ack DSC disconnection(Enable buttons) (0x34)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x34 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to disconnect with S/W.

- Return：The DSC has no return value.

5.1.43 Take shot in Fine (VCam) mode: 320x240 (0x3E)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x3E |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to take shot in Fine (VCam) mode: 320x240. This command can not save the image data on Internal Memory/CF-Card.

- Return：The DSC return the shot image data to host.

5.1.44 Set DSC in Fine (VCam) mode: 320x240 and set picture’s resolution (0x3F)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x3F |
| 2 | 1 |
| 3 | 0 |
| 4 | Image resolution value1 |
| 5 | Image resolution value2 |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set in Fine (VCam) mode: 320x240 and set picture’s resolution (if take a shot).

(value1, value2) :(0, 0) → it will take 320x240 resolution picture.

(0, 1) → it will take 640x480 resolution picture.

(1, 1) → it will take 1024x768 resolution picture.

‧Return：The DSC has no return value.

5.1.45 Take shot in Draft(VCam) mode: 320x80 (0x40)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x40 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to take shot in Draft(VCam) mode: 320x80. This command can not save the image data on Internal Memory/CF-Card.

- Return：The DSC return the shot image data to host.

5.1.46 Set DSC in VCam mode: 320x80 (0x41)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x41 |
| 2 | 0x01 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set in VCam mode: 320x80.

- Return：The DSC has no return value.

5.1.47 Set VCam mode: 320x80 AGC_gain (0x43)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x43 |
| 2 | 320x80 AGC value1 (Hi-byte) |
| 3 | 320x80 AGC value2 (Low-byte) |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set VCam mode: 320x80 AGC_gain.

- If in 320x80:

320x80 AGC_gain = AGC_gain;

- In ‘Fine mode’:

- If (786 - Exposure value) > 264

320x80 AGC_gain =

AGC_gain + (20 * (log10(( 786 – Exposure value) / 264))) / 0.0476;

- If (786 - Exposure value) <= 264

320x80 AGC_gain = AGC_gain;

- 320x80 AGC value1 = 320x80 AGC_gain >> 8;

320x80 AGC value2 = 320x80 AGC_gain & 0x00FF;

3. This value is used when really take a shot.

- Return：The DSC has no return value.

5.1.48 Set RGB Gain value (0x44)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x44 |
| 2 | R_Gain value |
| 3 | G_Gain value |
| 4 | B_Gain value |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set RGB_gain value in VCam mode.

- Return：The DSC has no return value.

5.1.49 Set Exposure value and Draft mode Exposure value (0x45)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x45 |
| 2 | Exposure value1 (Hi-byte) |
| 3 | Exposure value2 (Low-byte) |
| 4 | Draft mode Exposure value1 (Hi-byte) |
| 5 | Draft mode Exposure value2 (Low-byte) |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set Exposure Time and Draft mode Exposure Time.

1. In ‘Draft mode’:

- Exposure value → Min value is 0, Max value is 264.

- Draft mode Exposure value = 264 – (Exposure value)

→ Min value is 0.

2. In ‘Fine mode’:

- Exposure value → Min value is 0, Max value is 786.

- If (786 - Exposure value) > 264

→ Draft mode Exposure value = 0x108;

- If (786 - Exposure value) <= 264

→ Draft mode Exposure value = 786 - Exposure value;

3. Exposure value1 = Exposure value >> 8;

Exposure value2 = Exposure value & 0x00FF;

Draft mode Exposure value1 = Exposure value >> 8;

Draft mode Exposure value2 = Exposure value & 0x00FF;

4. Exposure value is used to set DSC by preview.

Draft mode Exposure value is used to set DSC if really to take a shot.

- Return：The DSC has no return value.

5.1.50 Set AGC_gain (0x46)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x46 |
| 2 | AGC value1 (Hi-byte) |
| 3 | AGC value2 (Low-byte) |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set AGC_gain by preview.

- Return：The DSC has no return value.

5.1.51 Get RGB_gain, AGC_gain, Exposure_Time setting (0x47)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x47 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to get RGB_gain, AGC_gain, Exposure_Time setting in VCam mode.

- Return：The DSC return 16 bytes data by EndPoint1. The first packet (8 bytes) is dummy data. The second packet (8 bytes) is not dummy data, and only 7 bytes is valid in second packet (8 bytes).

R_gain = Data[0];

G_gain = Data[1];

B_gain = Data[2];

AGC_gain = (Data[3] << 8) + Data[4];

Exposure_Time = (Data[5] << 8) + Data[6];

5.1.52 Get DSC Quality setting (0x49)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x49 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to get quality setting.

- Return：The DSC return 16 bytes data by EndPoint1. The first packet (8 bytes) is dummy data. The second packet (8 bytes) is not dummy data, and only first byte is valid in second packet (8 bytes). If the data is 0, then the image quality is Economic. If the data is 1, then the image quality is Standard. If the data is 2, then the image quality is High.

5.1.53 Set Exposure Mode (0x50)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x50 |
| 2 | Mode ID(0：MTRX, 1：CNTR) |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set exposure mode.

- Return：The DSC has no return value.

5.1.54 Get Exposure Mode (0x51)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x51 |
| 2 | 0 |
| 3 | 0 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to get exposure mode.

- Return：The DSC return 16 bytes data by Pipe2. Only first byte is valid. If the data is 1, the exposure mode is CNTR. If the data is 0, the exposure mode is MTRX.

5.1.55 Set image Saturation (0x52)

| Byte Offset | Host Command |
| --- | --- |
| 0 | 0x55 |
| 1 | 0x52 |
| 2 | Saturation value1 |
| 3 | Saturation value2 |
| 4 | 0 |
| 5 | 0xAA |
| 6 | 0 |
| 7 | 0 |

- Function：The command informs the DSC to set image saturation in VCam mode. The saturation value is from 0x00 to 0xFF, and normal value is 0x58. When send this command to DSC, the ‘Saturation value1’ and ‘Saturation value2’ must be equal.

- Return：The DSC has no return value.